## Slide 1: microbeam radiotherapy VERSUS conventional radiotherapy FOR Diffuse Intrinsic Pontine Glioma
L M Smyth, P A Rogers, J C Crosbie & J F Donoghue

## Slide 2: Clinical Radiotherapy
50% of cancer patients would benefit from RT (RANZCR 2015)
Curative vs Palliative
External vs Internal vs Systemic

## Slide 3: Clinical Radiotherapy
External beam vs Internal vs Systemic

## Slide 4: Clinical Radiotherapy
Temporal fractionation
t=0

## Slide 5: Clinical Radiotherapy
Temporal fractionation
t=0
t=30

## Slide 6: Synchrotron MICROBEAM Radiotherapy (MRT)
Australian Synchrotron – Imaging and Medical Beamline
Hutch 2B

## Slide 7: Microbeam RT vs Conventional RT
 | Conventional RT | MRT
Source | LINAC | Synchrotron
Typical radical doses | 40-70 Gy | 100-1000 Gy (Peak)
Dose Rate | ~0.1 Gy/second | ~300 Gy/second
Beam energy | Megavoltage | Kilovoltage
Fractionation | Temporal | Spatial
Dose Profile (cross section) |  | 
Notes: Comb analogy

## Slide 8: MRT
Parallel planar beams
25-50µm wide
200-400µm spacing
Normal tissue tolerance & tumour control
Image reproduced from Martinez-Rovira et al. (2012)
Notes: PVDR – depends on field size and depth in tissue. Decreases with bigger fields, and with depth due to effects of lateral and forward scatter in tissue. Typically valley = 10 Gy, Peak = 100 Gy, and this is what we anticipate this is in our therapeutic window.
Despite the highly inhomogenous fields, tumour control can be achieved
Radiobiology is extremely different to CRT – differential activation of gene pathway, and differential response of the immune system

## Slide 9
“What are equivalent doses??”
Notes: This is a key question! In terms of tumour control and normal tissue toxicity

## Slide 10: Why?
Improvements are still needed!
Advanced Lung Cancer
Pancreatic Cancer
DIPG (Grotzer et al. 2015)

## Slide 11: Diffuse Intrinsic pontine glioma (dipg)
Most deadly paediatric brain tumour, infiltrates brainstem
5-10 y/o - Loss of body control, cranial nerve palsies
Radiotherapy is the mainstay
8-14 months survival
Could MRT be an alternative?
Notes: - Due to location and diffuse/infiltrative nature of disease, surgery is not an option, and brainstem limits dose that can be delivered
- Despite changes to fractionation and addition of chemo, survival HAS NOT CHANGED significantly in the past 30 years.

## Slide 12: Aim & Methods
Determine dose-equivalence between MRT and Conventional RT (CRT)
Compare the radio sensitivity of two DIPG cell lines
Notes: Ie. Which cell lines might be a good candidate for MRT??

## Slide 13: Method
Two DIPG cell lines (JHH and SF7761)
Dose escalation
  CRT: 2 – 12 Gy
  MRT: 112 – 1180 Gy
Clonogenic Assay (Ibahim et al. 2014)
Apoptosis and Cell Cycle Assays

## Slide 14: Method - dosimetry
Table 1. Peak and valley doses at increasing depth in water for a 140 mm x 30 mm field size |  |  |  | 
Depth | Surface |  | 5mm | 
PVDR | 23.7 |  | 17.3 | 
 | PD (Gy) | VD (Gy) | PD (Gy) | VD (Gy)
 | 112.0 | 4.7 | 105.2 | 6.1
 | 250.0 | 10.6 | 234.7 | 13.5
 | 560.0 | 23.6 | 525.8 | 30.3
PVDR; Peak to valley dose ratio, PD; Peak dose, VD; Valley dose |  |  |  | 
Notes: PVDR – ratio of peak to valley dose. Decreases with increased field size and depth (due to scatter) ~ 24 for our experiments (140 x 30mm field size).
Verified MRT doses using HDV2 Gafchromic film, against a series of calibration films produced at 20mm depth and 20x20mm field size
Mean energy of MRT – 95KeV; 300 Gy/Sec in beam
CRT – Cobalt 60 ~1.3MeV; 2 Gy /minute

## Slide 15: Results
SF7761 cell line more sensitive to MRT & CRT
Fit these curves to linear quadratic model
Interpolated equivalent doses
* p<0.05, ** p<0.01
Notes: 14 day clonogenic assay
What we did was calculate equivalent doses using the linear quadratic dose-response model, which is accepted for radiotherapy, and non-linear regression.

## Slide 16: Results
Table 1. Interpolated equivalent CRT doses for increasing MRT doses |  |  | 
 | Equivalent CRT doses (Gy) |  | 
Cell Line | 112 Gy MRT | 250 Gy MRT | 560 Gy MRT
SF7761 | 3.2  0.3 | 6.8  0.4 | 9.1
JHH | 2.5  0.1 | 6.1  0.2 | 9.3  0.3

## Slide 17: Results - apoptosis
*p<0.05, **p<0.01
Notes: No Clear trend for JHH – CRT marginally higher than MRT but not significant at any point. MRT clearly higher for each equivalent dose for SF7761, with significance at 560 Gy versus 9 Gy – WHY!!!!???

## Slide 18: Results – cell cycle
JHH
SF7761
Control
250 Gy
Propidium Iodide
Percentage of Cells
Polyploidy
No Polyploidy

## Slide 19: Results – cell cycle
JHH
SF7761
Control
6 Gy
Propidium Iodide
Percentage of Cells
Polyploidy
No Polyploidy
A

## Slide 20
Polyploidy an important factor in treatment resistance (Coward et al. 2014, Erenpreisa et al. 2013)
JHH came from patient previously treated with chemo-radiotherapy  Evolution of treatment resistance?
DISCUSSION
Notes: JHH has mutant p53

## Slide 21: DISCUSSION

## Slide 22
Calculated dose-equivalence using DIPG cell lines
JHH  polyploidy  radio-resistance
MRT a possible alternative for radiosensitive DIPG types (SF7761)
In vivo normal tissue toxicity – next frontier in CRT-MRT dose-equivalence and progress to clinical trials
Conclusion
Notes: Our next step is to see if at equivalent doses for tumour kill (ie the doses in this study), there is less normal tissue toxicity for MRT

## Slide 23
Supervisors
Prof Peter Rogers
Dr Jeffrey Crosbie
Dr Jacqueline Donoghue
Australian Synchrotron - Imaging and Medical Beamline
Jayde Livingstone
Andrew Stevenson
Conclusion