## Slide 1
Dr James Tickner | Australian Accelerator Technology Forum
October 2020
Industrial photonuclear activation analysis of gold and other metals in mineral ores

## Slide 2: Assay in the gold industry
Slide 2 | Industrial photonuclear activation analysis of gold and other metals in mineral ores | James Tickner
2 |
Optimising the use of our Metal Resources | Dr James Tickner
+
Exploration
Resource development
Grade control and extraction
Stockpiling
Crushing and blending
Milling
Separation
Tails monitoring
Metal balance
Delineation
Extraction
Processing
Accuracy
Timeliness
$
Cost
Drivers
Large mine operation can generate > 1000 assays per day

## Slide 3: Traditional assay methods
Fire-assay has been the accepted analysis method for many centuries
Existing alternatives:
  Aqua regia digest, cyanidation, neutron analysis
Turn-around
> 24 hours
Small sample
(10-50 g)
Skilled labour requirements
Hazardous process
g
Extensive
prep
Slide 3 | Industrial photonuclear activation analysis of gold and other metals in mineral ores | James Tickner

## Slide 4: PhotonAssay technology
X-rays
Au
Au
Au
Au
Assay process takes < 2 min
Robot
shuttle
Crush to 2-3 mm
Split into jars
0.0 3/2+
77.4 keV 1/2+
268.8 keV 3/2+
279.0 keV 5/2+
409.2 keV 11/2-
t½ = 7.73 sec
197Au
8.5 MeV
8 kW
15 s irradiation
15 s measurement
Photonuclear reaction
Au197(g, g’)Au197M
279 keV g emission
Slide 4 | Industrial photonuclear activation analysis of gold and other metals in mineral ores | James Tickner

## Slide 5: Installation
First installation – Canning Vale, Perth
Slide 5 | Industrial photonuclear activation analysis of gold and other metals in mineral ores | James Tickner

## Slide 6: Accelerator design
Challenging environment
  Dust, temperature, remote location, spares availability
Continuous 24/7 operation
Turn-key operation
Dose and energy stability/monitoring
Radiation shielding
Custom electron linear accelerator manufactured by Nuctech Company Ltd (China)
  7-14 MeV end-point energy range
  8 kW maximum beam power
  160 Gy/min @ 1 m @ 8.5 MeV
  S-band Klystron RF source
  Proprietary Bremsstrahlung conversion target
Challenges
Slide 6 | Industrial photonuclear activation analysis of gold and other metals in mineral ores | James Tickner

## Slide 7: Beam intensity/energy variations
Target gold measurement accuracy better than 1-2%
Requires excellent beam stability and/or monitoring
Rely on simultaneous activation of gold in sample and bromine (207 keV g-ray emission) in reference disc
  Fully corrects for beam power
  Accurately corrects for beam energy
Slide 7 | Industrial photonuclear activation analysis of gold and other metals in mineral ores | James Tickner

## Slide 8: Radiation protection
Challenges:
  8.5 MeV X-ray source, 160 Gy/min, 24/7 operation
  Compact shield in shipping container
  Rapid sample access
  Turn-key operation for users
Solutions:
  Patented layered shield to manage X-ray, neutron and secondary gamma-ray emissions
  Patented automated ‘plug’ to allow sample ingress/egress in < 1 s
  Modular design to support service and maintenance access
  Robust arming and interlock procedures
Slide 8 | Industrial photonuclear activation analysis of gold and other metals in mineral ores | James Tickner

## Slide 9: Future: mine-site deployment
Accuracy
Timeliness
$
Cost
On-site deployment could reduce assay
turn-around time to under 30 mins
  Grade control
  Process control
One-cabin mine unit under development
  Smaller LINAC: 2 kW max power, 9 MeV max energy, magnetron RF source
  More compact shielding
  Fully automated internal monitoring and calibration
Slide 9 | Industrial photonuclear activation analysis of gold and other metals in mineral ores | James Tickner

## Slide 10
Dr James Tickner
Chief Technology Officer
+61 409 828 456
james.tickner@chrysos.com.au